## Slide 1: Overview of Madison’s Minimum Housing Code & Lead-Based Paint (LBP) Investigations
Created by Doug Dalsing Co-Owner, Testudo LLC

## Slide 2: Introduction
  Should be apparent that—YES—it is an inspection for meeting Madison’s minimum housing code
  Focus should be on the word “minimum”
    Level of detail is not comparable to a “home inspection” from a worthwhile home inspector
    & yes, there’s certainly overlap with home inspection criteria

## Slide 3: What is checked?
Presence of certain rooms
Makeup of certain rooms
Electrical
Heating
Health & Safety
Functionality of certain appliances, fixtures, components
Lead-based paint
Exterior
Mechanicals
Notes:     Lead-based paint
      “Are all interior/exterior surfaces either free of cracking, scaling, peeling, chipping, and loose paint or adequately treated and covered to prevent exposure of the occupants to lead based paint hazards?”

## Slide 4: Most common reasons inspections don’t pass
Lack of smoke & carbon monoxide detectors
Lack of window screens
Missing outlet covers
Inoperable windows (usually casement windows with broken hardware & rotted sashes)
Deteriorated lead-based paint
Missing or dilapidated hand rails
Electrical hazards (missing covers)
Plumbing issues

## Slide 5: Key definitions in WI’s lead-based paint (LBP) regulations
Residential requirements for LBP apply to homes built before 1978
Lead inspection, or risk assessment
  Comprehensive investigations that identify LBP
    Inspections stop at merely identifying LBP
    Risk assessments identify LBP hazards
Lead-safe remodeling or lead abatement
  Lead abatement is permanent elimination of lead hazards
  Remodeling can be completed in order to maintain components coated in LBP (& might incidentally eliminate lead hazards)
    Both require work to be completed by personnel certified by State of Wisconsin who hold a “blue card” before a clearance could proceed
Lead clearance
  Completed after remodeling or abatement work is finished in order to assess whether all LBP debris is cleaned up

## Slide 8
Please give a blank inspection form to your realtors ahead of time so they could address the easiest fixes beforehand
Contact the inspector, Doug Dalsing, with any questions: doug@TestudoOnline.com or (608) 205-8025